## Slide 1
September 12- 13,2018| NEPOOL Markets Committee
Catherine McDonough
413.535.4027| cmcdonough@iso-ne.com
Electric Storage Participation in Markets
FERC Order No. 841 Compliance

## Slide 2
FERC Order No. 841 Compliance
WMPP ID: 129
Filing Deadline: December 3, 2018
FERC Order No. 841 requires ISOs to establish a “participation model” (i.e., market rules) that facilitates the participation of Electric Storage Resources (ESRs) in RTO/ISO markets
  See Appendix B for a summary of participation model requirements
  Effective date for the Order: December 3, 2019
Enhanced Storage Participation changes (WMPP ID: 122), approved by the Participants Committee on August 24, largely (but not completely) meet the requirements of the Order
Additional tariff changes are required to:
  Lower the minimum size requirement for the participation model
  Make the participation model available to all storage technologies

## Slide 3: Overview of Today’s Presentation
Review tariff changes for the compliance filing to:
  Add new definitions
  Lower the minimum size requirement for the participation model
  Make the participation model available to all storage technologies
  Effective date for DARDs to participate in the Regulation Market
  Additional Clean-up
Begin overview of ISO compliance approach with review of how Electric Storage Facility (ESF) rules account for specific physical and operational characteristics described in FERC’s Order No. 841 (Section IV.E)
Respond to participant question
Respond to Participant Question
Review Compliance Tariff Changes
How ESF Rules Account for Physical and Operational Characteristics

## Slide 4: Tariff Changes
To Comply with FERC Order No. 841

## Slide 5: FERC Order No. 841 Compliance Changes
Overview of Changes to Market Rule 1
New definitions
  Available Energy and Available Storage
  Maximum Daily Energy Limit
Lower the minimum size requirement for ESFs
  Definition of Asset Related Demand (ARD)
  Electric Storage Facilities Section III.1.10.6 (a)
  Regulation Market Section III.1.14 (a)
Enable all technologies to participate under EFS rules
  Electric Storage Facilities Section III.1.10.6
Effective date for DARDs to participate in Regulation Market
  Modify definition of Regulation Resources
  Sections III.14 .2,III.14 .3, III.14.6, and III.14.8
Clean-up changes
  III.1.7.19.2.3.2 (c), III.1.10.1A (c)(v) and (vii),
  III.9.7.1 through III.9.7.2 , III.9.7.2 (a)(i) and (ii)

## Slide 6: FERC Order No. 841 Compliance Changes
New Definitions
Available Energy
  is a value that reflects the MWhs of energy available from an Electric Storage Facility for economic dispatch”
Available Storage
  is a value that reflects the MWhs of unused storage available from an Electric Storage Facility for economic dispatch of consumption
Maximum Daily Energy Limit
  is the maximum amount of megawatt-hours that a Limited Energy Resource expects to be able to generate in the next Operating Day

## Slide 7: FERC Order No. 841 Compliance Changes
Lower the Minimum Size Requirement
Asset Related Demand
  Lowering the size requirement for Storage DARDs to 0.1 MW
Section III.1.10.6 (a)
  New subsection (i) that says ESF “should have the ability to inject 0.1 MW and consume 0.1 MW”
  Sections re-numbered to accommodate addition of a new sub-section
Section III.1.14.2 (a)(ii) 1
  Replace Continuous Storage Facility with Electric Storage Facility because Order No. 841 requires 0.1 MW minimum size requirement for all resources using electric storage participation model (not just Continuous Storage Facilities).
    This change makes it clear that the minimum size requirement for Generator Assets not associated with the ESF model has not changed

## Slide 8: FERC Order No. 841 Compliance Changes
Lower the Minimum Size Requirement (continued)
III.1.14.2 (a)(iii) 2
  Add new subsection to drop minimum Regulation Capacity of Continuous Storage ATRRs and of Generator Assets associated with Binary Storage Facilities to 0.1 MW
III.1.14.2 (a)(ii) 3
  Delete “as a Generator Asset” because it is unnecessary and confusing
  Add reference to new subsection 2 so that the 1 MW minimum to provide Regulation Capacity does not apply to ESFs
  Delete phrase “no less than” because it is unnecessary

## Slide 9: FERC Order No. 841 Compliance Changes
Make ESF Rules Available to all Storage Technologies
III.1.10.6 (b)
  Delete (iii) requirement that Binary Storage Facility must “comprise one or more reversible hydraulic turbines” because the Order requires the storage participation model to be applicable to any storage technology
  Delete “and” from subsection (ii) and add “and” to subsection (i) to account for the deletion of subsection (iii)

## Slide 10: FERC Order No. 841 Compliance Changes
Effective Date for DARDs to Participate in Regulation Market
As part of the ISO’s review of the storage changes and FERC Order No. 841, it was identified that the ISO does not have the systems in place to support the ability for a DARD to provide regulation
The ISO is proposing to delay the effective date of the implementation of this functionality because of the significant effort to implement and lack of any requests or interest for a participant to regulate as a DARD
The proposed tariff language for December 2019 removes DARDs from the list of Regulation Resources and deletes tariff provisions that relate to a DARD’s ability to provide regulation (III.14.3 (a)(ii), III.14.3(a)(iii) and III.14.8(d))
The removed provisions, as well as additional provisions (II.14.2(a) (ii)(2), III.14.6(b) related to the BSF changes, will be filed with a future effective date; the ISO is evaluating the effective date for when these changes could be implemented

## Slide 11: FERC Order No. 841 Compliance Changes
Clean-up Changes
III.1.7.19.2.3.2 (c)
  Delete the term “Fast Start” following “shall be calculated” and before the term “Demand Response Resource” to make language consistent with subsection (b) and (c)(ii) of this provision
III.1.10.1A (c)(v)
  Removes term “available energy” from language describing Limited Energy Resources since Available Energy is now a defined term that is not relevant to this provision
III.1.10.1A (c)(vii)
  Change to clarify that a Supply Offer for all Generator Assets associated with ESFs (not just Continuous Storage Facilities) shall also meet the requirements specified in Section III.1.10.6

## Slide 12: FERC Order No. 841 Compliance Changes
Clean-up Changes (continued)
III.9.7.1 through III.9.7.2
  Revised numbering to reduce confusion
III.9.7.2 (a)(i) and (ii)
  Adds reference to “Demand Response Resources that have been dispatched” to language describing Target Activation MW for TMNSR and TMOR because the references to Demand Response Resources were inadvertently deleted in the Enhanced Storage Participation changes

## Slide 13: Electric Storage Facility Rules
How They Comply with FERC Order 841’s Requirement to Account for Physical and Operational Characteristics
(Section IV.E of Order)

## Slide 14: FERC Order No. 841
How ISO Market Rules Comply
Definition of Electric Storage Resource
Creation of a Participation Model for Electric Storage Resources
Eligibility of Electric Storage Resources to Participate in the RTO/ISO Markets
Participation in the RTO/ISO Markets as Supply and Demand
Physical and Operational Characteristics of Electric Storage Resources
State of Charge Management
Minimum Size Requirement
Energy Used to Charge Electric Storage Resources
Today: Review Compliance with Section IV.E
Next Time: Additional Compliance Discussion

## Slide 15: FERC Order No. 841- Requirement (Section IV.E)
General
ISO/RTO must demonstrate how its Storage Participation Model accounts for thirteen physical and operating characteristics of electric storage resources (ESRs) through bidding parameters or other means (Appendix A describes each characteristic)
ISO/RTO can determine whether submission of information by the ESR is mandatory or discretionary; submission of information must be consistent with how ISO/RTO accepts information from other resources
If ISO/RTO adopts bidding parameters to account for the physical and operational characteristics, ISO/RTO must permit the resource to submit the parameters in the day-ahead and real-time markets
Allowing storage model users to provide updated information through any applicable bidding parameters (consistent with other participants’ ability to do so) will help ensure that the RTO/ISO has necessary information to efficiently dispatch the system

## Slide 16: Electric Storage Facility Rules
Account for the Requisite Characteristics in the Real-time Energy Market (RTEM)
Physical Characteristic | Bidding Parameter or Telemetered Value*
State of Charge (%) | Available Energy & Available Storage (MWh)*
Maximum State of Charge (%) | Available Storage (MWh)*
Minimum State of Charge(%) | Available Energy (MWh) *
Minimum Charge Limit (MW) | Minimum Consumption Limit (MW)
Maximum Charge Limit (MW) | Maximum Consumption Limit (MW)
Minimum Discharge Limit (MW) | Economic Minimum (MW)
Maximum Discharge Limit (MW) | Economic Maximum (MW)
Minimum Charge Time | Minimum Run Time for Storage DARD
Maximum Charge Time | Available Storage*
Minimum Run Time | Minimum Run Time for Generator Asset
Maximum Run Time | Available Energy *
Charge Ramp Rate | Manual Response Rate for Storage DARD
Discharge Ramp Rate | Manual Response Rate for Generator Asset
* State variables telemetered to ISO but not included in Supply Offers or Demand Bids

## Slide 17: Electric Storage Facility Rules
Account for State of Charge via Telemetered Values in RTEM
ESFs are required to telemeter their Available Energy and Available Storage to the ISO every 4 seconds
Available Energy is a value that reflects the MWhs of energy available from an Electric Storage Facility for economic dispatch
Available Storage is a value that reflects the MWhs of unused storage available from an Electric Storage Facility for economic dispatch of consumption

## Slide 18: Electric Storage Facility Rules
Telemetered Values Ensure a Feasible Dispatch in the RTEM
  The ISO generally runs its dispatch software every 10 to 15 minutes
  To ensure that the dispatch is feasible, the Maximum Consumption Limit must be re-declared in real time to ensure that an ESF can consume at this limit for 15 minutes based on its Available Storage MWh
The Economic Maximum parameter must be re-declared in real time to ensure that the ESF has enough Available Energy to sustain operation for one hour. Doing so, enables the ISO to co-optimize the supply of energy and reserves and to comply with the NPCC’s one hour duration requirement for reserves

## Slide 19: Electric Storage Facility Rules
Telemetered Values Ensure a Feasible Dispatch in the RTEM (cont.)
If an ESF opts to self-dispatch, the Economic Maximum must be re-declared to ensure that the ESF can discharge at this rate for 15 minutes
  If the self-dispatch MW is greater than the MW discharge rate that can be sustained for one hour based on Available Energy, no reserves will be counted on the ESF
Resources (including Limited Energy Resources) do not submit a maximum run time or maximum charge time in the RTEM
  The maximum run time for an ESF is determined by its Available Energy
  The maximum charge time for an ESF is determined by its Available Storage

## Slide 20: Electric Storage Facility Rules
Account for all Requisite Characteristics in Day-ahead Energy Market
The day ahead energy market is economically optimized over a 24-hour period based on the bids of market participants
ESFs can bid the same parameters into the day-ahead energy market (DAEM) as they can bid into the RTEM
ESFs have two bid parameters that can be used to account for available energy and available storage in the DAEM:
  Maximum Daily Energy Limit (MWh)
    Maximum amount of energy the participant wants to sell for the entire operating day
  Maximum Daily Consumption Limit (MWh)
    Maximum number of MWhs that the participant wants to buy for the entire operating day

## Slide 21: Response to participant Question

## Slide 22: Response to Participant Question
Question: Can you confirm that a 1 MW/2 MWh storage resource, interconnected in front of the meter, would be able to qualify for 1 MW of Capacity, given the two hour audit, even though under the ISO’s automatic re-declaration of energy limits design, the resource would not be dispatched for 1 MW of energy for two hours?
ISO Response: If the storage device had 2 MWh of Available Energy at the beginning of the audit, the automatic re-declaration process would not hinder its ability to generate 1 MW for 2 hours. The Generator Asset would be placed into unit control mode (UCM) 3 (on line, non-dispatchable) at the beginning of the audit and would not be counted for reserves. This would enable the Generator Asset to discharge at 1 MW for two hours without regard to its re-declared Economic Maximum to meet the FCM audit requirement.

## Slide 23: Expected Stakeholder Schedule
FERC 841 Compliance
Stakeholder Committee and Date | Scheduled Project Milestone
Market Committee Discussion July 2018 | FERC Order 841 Requirements
Markets Committee Discussion August 2018 | Discuss Proposed Compliance Changes
Markets Committee September 2018 | Review Compliance Tariff Changes
Markets Committee October 2018 | Vote
Participants Committee November 2018 | Vote
Planned Effective Date: Q4 2019

## Slide 25: Appendix a
Physical and Operational Characteristics to be Accounted for in Storage Participation Model (Section IV.E of FERC Order)

## Slide 26: Storage Participation Model
Must Account for the State of Charge (SOC)
Characteristic | Definition
State of Charge | The amount of energy stored in proportion to the limit on the amount of energy that can be stored, typically expressed as a percentage. It represents the forecasted starting State of Charge for the market interval being offered into.
Maximum State of Charge | A State of Charge value that should not be exceeded (i.e., gone above) when a resource using the participation model for electric storage resources is receiving electric energy from the grid (e.g., 95% State of Charge). *
Minimum State of Charge | A State of Charge value that should not be exceeded (i.e., gone below) when a resource using the participation model for electric storage resources is injecting electric energy to the grid (e.g., 5% State of Charge).*
*Note: These values may either static values based on manufacturer specification or dynamic values depending on the operational
characteristics of the resource (e.g. if it is providing multiple services and needs to reserve part of its state of charge for another service)

## Slide 27: Storage Participation Model
Must Account for the Dispatch Limits
Characteristic | Definition
Minimum Charge Limit | The minimum MW level that a resource using the participation model for electric storage resources can receive from the grid.
Maximum Charge Limit | The maximum MW quantity of electric energy that a resource using the participation model for electric storage resources can receive from the grid.
Minimum Discharge Limit | The minimum MW output level that a resource using the participation model for electric storage resources can inject onto the grid.
Maximum Discharge Limit | The maximum MW quantity that a resource using the participation model for electric storage resources can inject to the grid.

## Slide 28: Storage Participation Model
Must Account for Intertemporal Constraints
Characteristic | Definition
Minimum Charge Time | The shortest duration that a resource using the participation model for electric storage resources is able to be dispatched by the RTO/ISO to receive electric energy from the grid (e.g., one hour).
Maximum Charge Time* | The maximum duration that a resource using the participation model for electric storage resources is able to be dispatched by the RTO/ISO to receive electric energy from the grid (e.g., four hours).
Minimum Run Time | The minimum amount of time that a resource using the participation model for electric storage resources is able to inject electric energy to the grid (e.g., one hour).
Maximum Run Time* | The maximum amount of time that a resource using the participation model for electric storage resources is able to inject electric energy to the grid (e.g., four hours).
*May be required to ensure that the duration of the dispatch is feasible

## Slide 29: Storage Participation Model
Must Account for Ramp Rates
Characteristic | Definition
Discharge Ramp Rate | The speed at which a resource using the participation model for electric storage resources can move from zero output to its Maximum Discharge Limit.
Charge Ramp Rate | The speed at which a resource using the participation model for electric storage resources can move from zero output to its Maximum Charge Limit.

## Slide 30: Appendix B
Summary of FERC Order No. 841 Requirements
(July Markets Committee)

## Slide 31: FERC Order No. 841
Eight Major Sections
Definition of Electric Storage Resource
Creation of a Participation Model for Electric Storage Resources
Eligibility of Electric Storage Resources to Participate in the RTO/ISO Markets
Participation in the RTO/ISO Markets as Supply and Demand
Physical and Operational Characteristics of Electric Storage Resources
State of Charge Management
Minimum Size Requirement
Energy Used to Charge Electric Storage Resources

## Slide 32: FERC Order No. 841
Summary of Requirements
  A. Definition of Electric Storage Resource
  Defines an electric storage resource (ESR) as “a resource capable of receiving electric energy from the grid and storing it for later injection of electric energy back to the grid.”
  B. Creation of a Participation Model for Electric Storage Resources
  Requires ISOs to establish a “participation model consisting of market rules that, recognizing the physical and operational characteristics of [ESRs], facilitates their participation in the RTO/ISO markets”; participation model should:
    Facilitate participation of ESRs and clearly specify qualification criteria
    Be available for all types of electric storage technologies
    Not preclude the use of existing models (i.e., Alternative Technology Regulation Resource, demand response)

## Slide 33: FERC Order No. 841
Summary of Participation Model Requirements
  C. Eligibility of Electric Storage Resources to Participate in the RTO/ISO Markets
  ESRs must be eligible to provide all capacity, energy and ancillary services that they are technically able to provide
  ESRs must be able to de-rate their capacity to meet the minimum duration requirements
  D. Participation in the RTO/ISO Markets as Supply and Demand
  ESRs must be able to set the market clearing price as a wholesale market seller and buyer
  ISO must prevent conflicting dispatch signals to an ESR
  ESRs are eligible to receive make-whole (Net Commitment Period Compensation) payments

## Slide 34: FERC Order No. 841
Summary of Participation Model Requirements (continued)
  E. Physical and Operational Characteristics of Electric Storage Resources
  Must account for 13 physical and operational characteristics through bidding parameters or other means
F. State of Charge Management
  Must allow ESRS to self-manage their state of charge
G. Minimum Size Requirement
  Must allow ESRs that are 0.1MW or larger to use participation model

## Slide 35: FERC Order No. 841
Other Requirements
H. Energy Used to Charge Electric Storage Resources
  “The sale of electric energy from RTO/ISO markets to an [ESR] that the [ESR] then resells back to those markets must be at the wholesale locational marginal price”
  ESRs should be exempt from transmission charges (normally allocated to load) when they are dispatched by the RTO/ISO to provide ancillary services
  Requires ISO to directly meter ESRs so all energy entering and exiting can be measured by that meter
    The Commission will also consider alternate proposals

## Slide 36: FERC Order No. 841
Initial Compliance Changes Identified By ISO
Allow Binary Storage Facility rules to be used by any storage technology that meets the qualification requirements (not just pumped-storage hydro)
Establish 0.1 MW size limit for all Electric Storage Facilities (i.e., Binary and Continuous Storage Facilities)
Define when Electric Storage Facilities are exempted from transmission charges

## Slide 37: Appendix C
Changes Required for Compliance Filing
(August Markets Committee Meeting)

## Slide 38: FERC Order No. 841
Participation Model Must Be Available to All Storage Technologies
The Electric Storage Facility (ESF) rules described in the recently proposed “Electric Storage” section of the tariff (Market Rule 1, Section III.1.10.6 (a through c) is a “storage participation model” that meets most of Order’s requirements
Under the ESF rules, a storage facility can participate as either a Binary Storage Facility (BSF) or a Continuous Storage Facility (CSF) depending on the facility’s physical characteristics
Any storage technology that meets the requirements can participate under the CSF rules, but the BSF rules are currently limited to only the pumped-storage hydro technology
As part of its compliance filing, the ISO will make the BSF rules available to all storage technologies
Other than the reduction in the minimum size requirement discussed below, no other changes to the BSF rules have been identified

## Slide 39: FERC Order No. 841
Minimum Size Requirement for Participation Model Must Be 100 kW
The Order states that its 100 kW minimum size requirement “applies to all minimum capacity requirements, minimum offer to sell requirements, and minimum bid to buy requirements” for electric storage resources that use the “participation model”
Order has no minimum size requirement with regard to MWhs of storage capacity
To comply with the Order, the ISO will lower the minimum size threshold for Generator Assets, DARDs and ATRRs associated with Electric Storage Facilities from 1 MW to 100 kW
Because the Forward Reserve Market (FRM) is portfolio (not resource ) based, the ISO will lower the minimum bid threshold for the FRM from 1 MW to 100 kW

## Slide 40: FERC Order No. 841
Implication of Lower Minimum Size Requirement for ESFs
Electric Storage Facilities (ESFs) can bid/offer a minimum of 100 kW as Generator Asset and/or DARD into the Day-Ahead Energy Market Real Time Energy Market
All Participants (including ESFs) can take on a 100 kW FRM obligation; Participants can already assign a DARD or Generator Asset in 100 kW increments to meet a FRM obligation
ESF Generator Assets can offer 100 kW of qualified capacity into the Forward Capacity Market (FCM)
ESFs can offer 100 kW of capacity into the Regulation Market
No change in ESFs ability to provide Black Start Service or VAR since there is no minimum size requirement to offer these services

## Slide 41: FERC Order No. 841
No Change to Bid/Offer Granularity in any Market
Resources can currently offer in:
  100 kW increments over the minimum size threshold in the energy and regulation markets
  1 kW increments over the minimum bid threshold in the FRM and FCM
The Order does not require and the ISO is not proposing any change to bid/offer granularity in any market

## Slide 42: Acronyms used
AGC – Automatic Generation Control
ATRR – Alternative Technology Regulation Resource
BSF – Binary Storage Facility
CSF – Continuous Storage Facility
ESF – Electric Storage Facility (BSF or CSF)
DAEM – Day-ahead Energy Market
DARD – Dispatchable Asset Related Demand
ESR – electric storage resource
FERC – Federal Energy Regulatory Commission
FCM – Forward Capacity Market
FRM – Forward Reserve Market

## Slide 43: Acronyms used (continued)
NPCC – Northeast Power Coordinating Council
PC – Participants Committee
RC – Reliability Committee
RTEM – Real-time Energy Market
RTO – Regional Transmission Organization
TC – Transmission Committee